## Slide 1
Digital Optics and Machine Learning algorithms for
Aircraft Maintenance
Salvatore Merola
Ph.D. student in Industrial Engineering
salvatore.merola@unina.it|savimerola@outlook.it
Department of Industrial Engineering
University of Naples Federico II
Via Claudio 21, 80125, Naples, IT

## Slide 2: Artificial Intelligence, Machine learning, Deep Learning,
Computer vision
Computer vision.

## Slide 3: A little bit of history…

## Slide 4: A little bit of history…
Early Beginnings (50s – 70s)
Rosenblatt’s Perceptron:

## Slide 5: A little bit of history…
Edge detections and Feature extraction(70s – 2000)

## Slide 6: A little bit of history…
Deep Learning revolution (2000 - now)
Convolutional Neural Networks (AlexNet, VGGNet, ResNet, … , YOLO)

## Slide 7: Computer vision

## Slide 8: Computer vision
How does it work?
Image acquisition : How? What acquisition system to use? What kind of images am I going to analyze?
Pre-Processing : Analysis Preparation phase (Data Augmentation)
          Noise Reduction
          Image Enhancement
          Resizing/Cropping
          Normalization

## Slide 9: Computer vision
How does it work?
Feature Extraction and representation:
Edges,
Corners,
Textures,
Colors,
Shapes,
…

## Slide 10: Computer vision
How does it work?
Deep Learning for Output Phase :
Object Detection
Image segmentation
Pose estimation

## Slide 11: Areas of applications

## Slide 12: Areas of applications
Technology fields
Automotive: Autonomous Vehicle (AV) , License Plate Recognition (LPR), …
Healthcare: medical images, diagnostic imaging, remote patient monitoring, …
Manufacturing: Quality control, Robotic automation, Predictive maintenance, …
Agriculture: Precision agriculture, livestock monitoring, pest control, …
…
And Aircraft field?

## Slide 13: Application on Aircraft: Maintenance Tasks

## Slide 14: Classical aircraft maintenance process
Aircraft maintenance processes
Maintenance Steering Groups (MSG) – 3 :
MSI determination (Maintenance Significant Items, critical components)
MSG-3 Analysis Level 1 (evaluating functional failure & possible consequences)
MSG-3 Analysis Level 2 (identifying possible maintenance actions)
Over 80% of inspections on large transport category aircraft are visual inspections. Small transport and general aviation aircraft rely on visual inspection techniques more heavily than large transport aircraft.
So in this presentation, visual inspection is the focus.

## Slide 15: New aircraft maintenance process
Aircraft maintenance processes

## Slide 16: Acceptability criteria for rivets
Aircraft maintenance processes
acceptable rivet when:
acceptable rivet when:
Cracks don’t cross on rivet’s head
From ref 51-11-11 Description Allowable Damage:

## Slide 17: Acceptability criteria for dents
Aircraft maintenance processes
From ref 51-11-13 Allowable Damage Limits for Dents - Generic:
So far, only dents complying with the regulations were captured.

## Slide 18: Methodology

## Slide 19: Digital optics trade-off phase
Methodology
Test with Drone as
acquisition system
 | Acquisition systems |  | 
 | Smartphone (12 MP) | Drone (4 MP) | Reflex (24 MP)
D = 65 cm |  |  | 
D = 75 cm |  |  | 
D = 85 cm |  |  | 
D = 100 cm |  |  | 
Red = Poor n. classifications
Yellow = Mediocre n. classifications
Green = Good n. classifications
Test with Reflex as
acquisition system

## Slide 20: YOLO v8 architecture
You Only Look Once algorithm

## Slide 21: Damage detection algorithm

## Slide 22: Database creation for training phase
Damage detection algorithm
Database | Condition | Missing rivets (n. of images) | Corroded rivet (n. of images) | General damage (n. of images)
Images from a full-scale fuselage section of a general aviation aircraft in white paint | Light | 60 | 19 | 33
 | Low light | 51 | 20 | 23
 | Blurred | 80 | 79 | 47
Images from a full-scale fuselage section of a commercial aviation aircraft in primer paint | Light | 74 | 34 | 12
 | Low light | 143 | 15 | 13
 | Blurred | 208 | 22 | 31
TOT. images for each defect |  | 616 | 189 | 159
TOT. database’s images |  | 964 |  | 
full-scale fuselage section of a commercial aviation aircraft in primer paint
full-scale fuselage section of general aviation aircraft in white paint

## Slide 23: Training options for YOLO algorithms
Damage detection algorithm
N. of classes | 3 (eroded_rivet, no_rivet, general_damage)
Training algorithm | ADAM (adaptive moment estimation)
Batch size | 16
Initial Learning Rate | 10-6
Epochs | 50
Training dataset | Approximately 6000 ROI
These ROIs include "noise" damage to make the network more robust.
Training Process
1018
1030
1
41
204
201
410
86
335
566
29

## Slide 24: Training process
Chart: Learning Rate vs Epochs
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
lr/pg0 | 0.00040012 | 0.0007984 | 0.0011803 | 0.0013441 | 0.0013441 | 0.0013158 | 0.0012875 | 0.0012592 | 0.0012309 | 0.0012026 | 0.0011744 | 0.0011461 | 0.0011178 | 0.0010895 | 0.0010612 | 0.0010329 | 0.0010046 | 0.00097629 | 0.000948 | 0.0009197 | 0.00089141 | 0.00086312 | 0.00083482 | 0.00080653 | 0.00077823 | 0.00074994 | 0.00072164 | 0.00069335 | 0.00066506 | 0.00063676 | 0.00060847 | 0.00058017 | 0.00055188 | 0.00052359 | 0.00049529 | 0.000467 | 0.0004387 | 0.00041041 | 0.00038211 | 0.00035382 | 0.00032553 | 0.00029723 | 0.00026894 | 0.00024064 | 0.00021235 | 0.00018406 | 0.00015576 | 0.00012747 | 9.92e-05 | 7.09e-05
lr/pg1 | 0.00040012 | 0.0007984 | 0.0011803 | 0.0013441 | 0.0013441 | 0.0013158 | 0.0012875 | 0.0012592 | 0.0012309 | 0.0012026 | 0.0011744 | 0.0011461 | 0.0011178 | 0.0010895 | 0.0010612 | 0.0010329 | 0.0010046 | 0.00097629 | 0.000948 | 0.0009197 | 0.00089141 | 0.00086312 | 0.00083482 | 0.00080653 | 0.00077823 | 0.00074994 | 0.00072164 | 0.00069335 | 0.00066506 | 0.00063676 | 0.00060847 | 0.00058017 | 0.00055188 | 0.00052359 | 0.00049529 | 0.000467 | 0.0004387 | 0.00041041 | 0.00038211 | 0.00035382 | 0.00032553 | 0.00029723 | 0.00026894 | 0.00024064 | 0.00021235 | 0.00018406 | 0.00015576 | 0.00012747 | 9.92e-05 | 7.09e-05
lr/pg2 | 0.00040012 | 0.0007984 | 0.0011803 | 0.0013441 | 0.0013441 | 0.0013158 | 0.0012875 | 0.0012592 | 0.0012309 | 0.0012026 | 0.0011744 | 0.0011461 | 0.0011178 | 0.0010895 | 0.0010612 | 0.0010329 | 0.0010046 | 0.00097629 | 0.000948 | 0.0009197 | 0.00089141 | 0.00086312 | 0.00083482 | 0.00080653 | 0.00077823 | 0.00074994 | 0.00072164 | 0.00069335 | 0.00066506 | 0.00063676 | 0.00060847 | 0.00058017 | 0.00055188 | 0.00052359 | 0.00049529 | 0.000467 | 0.0004387 | 0.00041041 | 0.00038211 | 0.00035382 | 0.00032553 | 0.00029723 | 0.00026894 | 0.00024064 | 0.00021235 | 0.00018406 | 0.00015576 | 0.00012747 | 9.92e-05 | 7.09e-05
Chart: Loss Functions
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
bbox_loss | 2.2001 | 1.8736 | 1.898 | 1.8163 | 1.8148 | 1.7763 | 1.7889 | 1.7706 | 1.7232 | 1.7343 | 1.7353 | 1.7446 | 1.7433 | 1.6909 | 1.6482 | 1.6471 | 1.695 | 1.6825 | 1.6638 | 1.6507 | 1.6332 | 1.636 | 1.6377 | 1.6181 | 1.5683 | 1.5961 | 1.6203 | 1.5994 | 1.5684 | 1.5696 | 1.5749 | 1.5816 | 1.5435 | 1.5619 | 1.557 | 1.5443 | 1.5129 | 1.553 | 1.5307 | 1.5229 | 1.5249 | 1.5119 | 1.5185 | 1.492 | 1.4698 | 1.4673 | 1.4792 | 1.4412 | 1.4504 | 1.4711
classification_loss | 3.4508 | 2.4258 | 2.1365 | 2.0988 | 2.0193 | 1.918 | 1.8047 | 1.7909 | 1.7209 | 1.6017 | 1.6253 | 1.5989 | 1.6093 | 1.5543 | 1.4354 | 1.4986 | 1.5033 | 1.4604 | 1.4127 | 1.4131 | 1.4226 | 1.383 | 1.3847 | 1.3289 | 1.2905 | 1.3274 | 1.3195 | 1.3034 | 1.3233 | 1.2363 | 1.2087 | 1.2617 | 1.1898 | 1.1956 | 1.2137 | 1.1323 | 1.1451 | 1.1275 | 1.1344 | 1.1277 | 1.124 | 1.0848 | 1.0689 | 1.0628 | 1.0249 | 1.0329 | 1.0443 | 0.97591 | 0.98771 | 0.98879
Chart: Recall Function
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
Recall | 0.21406 | 0.27301 | 0.15248 | 0.22653 | 0.22768 | 0.27556 | 0.38902 | 0.40314 | 0.43811 | 0.34086 | 0.49907 | 0.47404 | 0.53992 | 0.42202 | 0.4974 | 0.45413 | 0.4734 | 0.5236 | 0.53512 | 0.50287 | 0.54394 | 0.56472 | 0.50961 | 0.56176 | 0.52862 | 0.52911 | 0.58508 | 0.58534 | 0.57157 | 0.5281 | 0.5932 | 0.58426 | 0.6217 | 0.62663 | 0.66124 | 0.65411 | 0.64986 | 0.65135 | 0.65738 | 0.68916 | 0.68161 | 0.66784 | 0.67093 | 0.65637 | 0.69569 | 0.68453 | 0.68784 | 0.69637 | 0.69431 | 0.69671
Chart: Precision Function
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
Precision | 0.00386 | 0.21841 | 0.23582 | 0.22395 | 0.23925 | 0.29631 | 0.40436 | 0.46778 | 0.46039 | 0.45724 | 0.54237 | 0.55207 | 0.50085 | 0.4806 | 0.60546 | 0.57955 | 0.55477 | 0.6071 | 0.6536 | 0.62886 | 0.68024 | 0.61975 | 0.63498 | 0.68464 | 0.69513 | 0.60184 | 0.6985 | 0.71024 | 0.64997 | 0.63999 | 0.71068 | 0.7637 | 0.73402 | 0.74841 | 0.69833 | 0.80121 | 0.7699 | 0.76326 | 0.78092 | 0.79553 | 0.75095 | 0.78691 | 0.81858 | 0.77974 | 0.80801 | 0.7899 | 0.79452 | 0.7927 | 0.82908 | 0.81768

## Slide 25: Results from testing phase
Test image 1 before processing
Test image 1 after processing
Damage detection algorithm

## Slide 26: Results from testing phase (cont.)
Test image 2 before processing
Test image 2 after processing
Damage detection algorithm

## Slide 27: Results from testing phase (cont.)
Test image 3 before processing
Test image 3 after processing
Damage detection algorithm

## Slide 28: Results from testing phase (cont.)
Test image 4 before processing
Test image 4 after processing
Damage detection algorithm

## Slide 29: Effect of n. of epochs on training phase
- Misclassification (good rivets classified as missing rivets, with an accuracy > 65% )
- Corrosion not detected
- No Misclassification
- Corrosion detected
1st training epochs: 100
2nd training epochs: 1000

## Slide 30: More examples

## Slide 31: More examples
Errors in decal

## Slide 32: More examples
Errors in decal

## Slide 33: More examples
Damages on composite panels
Test 1 (No light, 90 deg angle, high-definition)

## Slide 34: More examples
Damages on composite panels
Test 2 (No light, 45 deg angle, high-definition)

## Slide 35: More examples
Damages on composite panels
Test 3 (Light, 90 deg angle, low-definition)

## Slide 36: And in the “future”…?

## Slide 37: Future Developments

## Slide 38
Thank you
for the attention
Salvatore Merola
Ph.D. student
salvatore.merola@unina.it
savimerola@outlook.it
Department of Industrial Engineering
University of Naples Federico II
Via Claudio 21, 80125, Naples, IT